Remaining work:
- Assemble his second PCB (took about 1.5 hrs to assemble the first one), but he knows how to do it now.
- Finish a working version of his code.
- Assemble a dipole antenna tuned to 70 cm or get a rubber duck with some RG-316 cable for the balloon station.  Prepare a 70 cm antenna with the right adapter and a way to mount his electronics to the antenna, as well as a tripod for the antenna.  We might have most of this at NEST, but he needs to be driving the effort to get it all together.
- Test a way for him to know which way to aim the ground station antenna during the flight.

Goal:
- Test ability to send two way signals from ground to high altitude balloon using LoRa at 433 MHz.
- There will be a ground station and a balloon mounted station.

Components:
- Arduino Nano
- Micro SD card read/write breakout board
- BME280 breakout board (temp/pressure/humidity)
- Adafruit RFM96W LoRa Radio Transceiver Breakout - 433 MHz (link)

Software Requirements:
- Balloon station should record a packet of information at regular intervals to a CSV file, containing:
  - millis() - time since starting up the device
  - pressure - to be used later to convert to altitude.  May as well record temp and humidity as well, since he already has it in the code.
  - 1 or 0 - was a new LoRa packet received since last entry
  - Transmission ID - this number is sent from the ground with each transmission (this is the hard part, and can be left for last)
  - Send a reply (ideally containing the transmission ID)
- Ground station should also record packets, containing:
  - millis()
  - 1 or 0 - was a new LoRa reply received since last packet
  - Transmission ID received (this is the hard part, and can be left for last)
  - Transmission ID sent

Software process:
- He has available to him the Adafruit example code for 2 way communications using the RFM9x breakout boards
- Workshop code we did earlier in the year to log various data collected from the BME280 to a concatenated packet in a CSV file.
- Recommended process:
  - If he doesn't have this working yet, the first step should be combining these two pieces of code into one.
  - Then he can modify the contents of the concatenated packet.
  - Add a variable for millis() - that's easy
  - Add a variable on ground station for transmission ID sent - also easy
  - 1 or 0 - was a new LoRa packet received since last packet - fairly easy
  - Transmission ID received is a little trickier.  He'll need to pull that out of the received packet and get it into the right data type. (I'd recommend getting all the rest done first.  Could be optional.)

Reference material:
Here is a link to the presentation from last year.  The section for the individual students starts on slide 17: https://docs.google.com/presentation/d/10H4d3TfIrMTZT0s1yK1EBnVWrM1x1FyKfmhBG6_SEs8/edit?usp=sharing

Practice your presentation:
- We ask that everyone does two practice presentation sessions with us, so we have a chance to give notes and suggestions after the first one.
- For a public presentation like this, we recommend people practice at home many times as well and try to improve each time.  It's only 1-2 minutes long, so a couple rehearsals a day is pretty reasonable.